## Slide 2: dragonflow简介
肖宏辉 华为技术有限公司
IRC： xiaohhui

## Slide 3: What is dragonflow?
Integral part of OpenStack Neutron
Fully Open Source
  https://launchpad.net/dragonflow
Lightweight Distributed SDN Controller with pluggable database

## Slide 4: What is dragonflow?
Dragonflow architecture consists of Neutron plugins which maps the Neutron models to new logical topology models
Dragonflow synchronizes this with local Dragonflow controllers which are distributed at each of the compute nodes using a pluggable distributed DB solution.

## Slide 5: Dragonflow architecture

## Slide 6: Data synchronization in Dragonflow

## Slide 7: Dragonflow VS Neutron legacy
Eliminate neutron agents
Use pub/sub Mechanism to notify compute node about the change
Distribute the control plane to compute nodes

## Slide 8: DHCP

## Slide 9: Neutron DHCP Implementation
Network Node
DHCP
namespace
DHCP
namespace
DHCP
namespace
DHCP
namespace
DHCP
namespace
dnsmasq
DHCP Agent
Neutron Server
Message Queue
Example
100 Tenants
3 vNet / tenant
= 300 DHCP Servers

## Slide 10: Dragonflow Distributed DHCP
1 | VM Send DHCP_DISCOVER
2 | Classify Flow as DHCP, Forward to Controller
3 | DHCP App sends DHCP_OFFER back to VM
4 | VM Send DHCP_REQUEST
5 | Classify Flow as DHCP, Forward to Controller
6 | DHCP App populates DHCP_OPTIONS from DB/CFG and send DHCP_ACK
DHCP DISCOVER
VM
DHCP SERVER
DHCP OFFER
DHCPREQUEST
DHCPACK
1
3
4
6
7
Compute Node
Dragonflow
VM
OVS
VM
1
2
br-int
qvoXXX
qvoXXX
OpenFlow
1
4
2
5
7
Dragonflow Controller
Abstraction Layer
L2 App
L3 App
DHCP App
SG
3
6
Pluggable DB
Layer
DB

## Slide 11: Security Group

## Slide 12: Security Groups in Neutron
Data plane performance
  Additional Linux Bridge on the Path
  Iptables
Control plane performance
  Rules needs to be re-compiled on port changes
    Many rules due to security group capabilities
  Iptable commands issued by CLI process
  RPC bulks
Notes: <voice note: Here we'd explain the part about them being vendor specific makes that each Neutron vendor would have to make its own implementation of libnetwork or cni reinventing the wheel and without the ability to share the common parts./>

## Slide 13: Security Groups in Dragonflow
Linux Bridge
Iptables
Openflow
Notes: <voice note: Here we'd explain the part about them being vendor specific makes that each Neutron vendor would have to make its own implementation of libnetwork or cni reinventing the wheel and without the ability to share the common parts./>

## Slide 14: Security Groups Translations
Direction:Egress
Type:IPv4, IP Protocol:TCP, Port Range:Any, Remote IP Prefix:0.0.0.0/0 match:ct_state=+new+trk,tcp,reg6=X actions=ct(commit,zone=network),resubmit(,<next_table>)
Direction:Ingress
Type:IPv4, IP Protocol:TCP, Port:22, Remote Security Group: Y
match:ct_state=+new+trk,tcp,reg6=X,reg7=Y, tp_dst=22
actions=ct(commit,zone=network),resubmit(,<next_table>)
Openvswitch:
CT（connection tracking）
Conjunction
Notes: <voice note: Here we'd explain the part about them being vendor specific makes that each Neutron vendor would have to make its own implementation of libnetwork or cni reinventing the wheel and without the ability to share the common parts./>

## Slide 15: Distributed Virtual Router

## Slide 16: East to West
OVS
VM
Compute Node
OVS
VM
Compute Node
OVS
Compute Node
Router
Namespace
Neutron(DVR)
Dragonflow
namespace
openflow
Router
Namespace
OVS
VM
Compute Node
VM
OpenFlow
OpenFlow
Notes: <voice note: Here we'd explain the part about them being vendor specific makes that each Neutron vendor would have to make its own implementation of libnetwork or cni reinventing the wheel and without the ability to share the common parts./>

## Slide 17: Floating IP
br-int
VM
Compute Node
Public
network
br-int
VM
Compute Node
Public
network
Neutron(DVR)
Dragonflow
namespace
openflow
Router
Namespace
Fip
Namespace
br-ex
br-ex
Notes: <voice note: Here we'd explain the part about them being vendor specific makes that each Neutron vendor would have to make its own implementation of libnetwork or cni reinventing the wheel and without the ability to share the common parts./>

## Slide 18: Dragonflow Roadmap
Additional DBs Drivers…
Pluggable Pub/Sub Mechanism
DB Consistency
Multi-segments support
Distributed SNAT
Advanced services

## Slide 19: Join the project Dragonflow
Documentation
https://wiki.openstack.org/wiki/Dragonflow
Bugs & blueprints
https://launchpad.net/dragonflow
DF IRC channel
#openstack-dragonflow
Weekly on Monday at 0900 UTC in #openstack-meeting-4 (IRC)